## Slide 1
ABBA firmware (and partition) status
Alessandra Camplani – Università degli Studi di Milano
19/07/2016

## Slide 2
Improvements in the firmware
2
Last presented version:
  Front FPGA: Version v0.96c
  Back FPGA: Version v0.69a1
New versions:
  Front FPGA: Version v0.96c1/ v0.96c2
    merging and reworking some common vhdl files (Thanks to Philipp!)
  Front FPGA: Version v0.96d
    Released version after tests in EMF
    Tested at EMF, but not applied yet in USA15 (same functionality of v0.96c)
  Back FPGA: Version v0.69a2
    Again, merging and reworking some common vhdl files (Re- thanks to Philipp!)
  Back FPGA: Version v0.69b
    Released version after tests in EMF
    Tested at EMF, but not applied yet in USA15 (same functionality of v0.69a)

## Slide 3
Tests for the new firmware in EMF
3
The new firmware version has been tested in EMF, taking some calibration runs.
One FPGA (remained) and used for this purpose.
The pulse is still here! 
FPGA #1
FPGA #0
Back
IP 168.192.10.4
Some more details: EMF run 303830
high ramp
#events 1000
#sample 60
latency 0x45

## Slide 4
Latency settings
4
Some calibration runs, with different latency seettings, have been taken in USA15.
For more details you can look here.
The position of the pulse (Lpeak) has been checked for each run (thanks to Adriana!).
The test confirmed that: a shift of 1 BC corresponds to a shift of 1 unit for the latency value.
So for example from an initial setting of 0x56 (86 in decimal):
to shift the pulse 10 BC to the right: increase the latency setting by 10, hence set it to 0x60 (96 in decimal)
- to shift the pulse 10 BC to the left: decrease the latency setting by 10, hence set it to 0x4C (76 in decimal)
Furthermore, the change in the number of samples doesn’t modify the pulse position in the readout window.
The number of samples moves the right end of the readout window: the left side of the window (Lmin) is fixed, while the right side (Lmax) is varied by modifying this value.

## Slide 5
System latency differences
5
The latency settings correspond to a specific position in the readout window, but this position can be different depending on the hardware chain.
For the following different scenarios, the very same latency setting will show up the pulse in different positions:
Physics runs vs. calibration runs in USA15
  The difference between the pulse peak in physics runs and calibration runs in USA15 is of ~10 BC:
  LPhypeak + 10 BC = LCalibpeak
BNL LTDB vs. LAL LTDB in USA15
  The difference between the pulse peak from the BNL LTDB and from the LAL LTDB in USA15 is of ~8 BC:
  LBNLpeak + 8 BC = LLALpeak
Calibration in EMF vs. calibration in USA15
  The difference between the pulse peak in calibration runs in EMF and in USA15 is of ~15 BC:
  LEMF-Calibpeak + 15 BC = LUSA15-Calibpeak
Now documented in the Twiki !!

## Slide 6
System latency now
6
BNL LTDB vs. LAL LTDB in USA15
  The difference between the pulse peak from the BNL LTDB and from the LAL LTDB in USA15 is of ~8 BC:
  BNLpeak + 8 BC = LALpeak
Latency settings have been changed to have all the pulses (of ~ 30 samples) recorded with ABBA starting at around sample 10 (the peak will be at sample 12).
  The two different LTDBs now have specific settings (here all the details):
  - 0x44 for LAL LTDB (FPGAs 18:2 and 19:1)
  - 0x4d for BNL LTDB (FPGAs 19:2 and 20:2)

## Slide 7
Front End issue
7
On July 12 first issue with FE (during the calibration runs)
  BNL LTDB links all unlocked: issue solved using some python scripts provided by BNL group
On July 15 again the same issue (during the latency setting change)
  BNL LTDB links again all unlocked: this time the python scripts didn’t work
  Most of LAL LTDB links were locked
On July 18 the situation was not improving
  BNL LTDB was still unlocked
  Most of LAL LTDB links unlocked. Tried reconfiguration of LTDB with some scripts (already tested and working) provided by Stefan Simion: configuration completely failed.
  All the LTDB links were unlocked
  FINALLY SOLVED!
    BNL LTDB - After re-powering the GLIB card, the python scripts were working again
    LAL LTDB - Stefan stopped the monitoring of the link status: this was causing a conflict with the reconfiguration
All the details here, here and here

## Slide 8
Conclusion and outlook
New firmware versions (front and back):
  Merging and reworking some common vhdl files
Latency issue solved
  Latency: found a fine position for the pulse fot both LTDBs and finally documented on the Twiki
FE issues solved
  After re-powering GLIB card and reconfiguration of BNL LTDB: link status is ok
  After stopping the monitoring of the LAL LTDB link status and after its reconfiguring: link status is ok
8