## Slide 1: Phase-I Trigger Readout Electronics Upgrade for the ATLAS Liquid-Argon Calorimeters
TIPP17 – ? MAY 2017
Alessandra Camplani – Universita’ degli studi and INFN Milano
On behalf of the ATLAS Liquid Argon Calorimeter group

## Slide 2: Outline
Introduction
  LHC, ATLAS, LAr
  Phase I Upgrade
LAr Front End Electronics
LAr Back End Electronics
Demonstrator
Summary

## Slide 3
Introduction

## Slide 4: Context – LHC and ATLAS
Large Hadron Collider (LHC) at CERN, Geneva, Switzerland
  27km circumference
  depth between 50 to 175m
  four collision points
ATLAS: A Toroidal LHC ApparatuS
  46m long, 25m diameter and 7000 tons
Purpose:
  Answer fundamental physics questions
  Standard model

## Slide 5: The Liquid Argon (LAr) Calorimeter
The LAr calorimeter is a sampling calorimeter with accordion-shaped lead absorbers and copper-kapton electrodes.
180K channels for the full readout of the electromagnetic (EMB+EMEC), hadronic (HEC) and Forward (Fcal) calorimeters
3K channels for analog Trigger readout
Front End crates: ≈ 1600 Front End Boards (FEB)
Back End crates: 200 Readout Out Driver boards (ROD)

## Slide 6: The current electronics
Regular readout:
Cells signals are amplified, shaped, sampled at 40MHz, digitized and transmitted at 100 kHz upon level-1 trigger
Trigger readout:
Summing signals on Layer Sum Board (LSB) to form trigger towers
Tower Builder Board (TBB) sums analog signals from LSB to send to L1 Calo system

## Slide 7: LHC Schedule
Two phase upgrade planned for LHC, ATLAS upgrade:
Phase-I (2021-2023): upgrade of trigger path, installation in 2019-2020
  (Average number of vertices per bunch crossing)
  Keep trigger max 100 KHz, latency
Phase-II (after 2025): upgrade of data path, installation in 2024-2025
  (Average number of vertices per bunch crossing)
  Keep trigger max 1 MHz, latency
Upgrade of LAr trigger readout
Upgrade of LAr main readout

## Slide 8: Calorimeter Upgrade
Trigger Tower
Super Cells
LAr Phase 1
Upgrade
LAr Phase-I upgrade: new calorimeter trigger electronics with increased granularity and functionality for LAr calorimeter level 1 trigger
Trigger Tower to Super Cells:
  Granularity increased 10 times per each trigger tower
  Provided information for each calorimeter layer for the full η range
  Finer segmentation in the front and middle layers of the EM barrel and endcap
  Higher resolution and shower information
Deal with the luminosity increase, maintaining a low-pT lepton threshold and keeping the same trigger bandwidth

## Slide 9: LAr Phase-I Project
Baseplane
Layer Sum Board
(LSB)
LAr Trigger Digitizer
Board (LTDB)
LAr Digital Processing System (LDPS)
New elements are highlighted in RED

## Slide 10
Front-End (FE) Upgrade

## Slide 11: FE electronics components
New Layer Sum Boards (LSB) to perform analog sums for super cells
New Baseplane to keep compatibility with existing setup
LAr Trigger Digitizer Boards (LTDB) with radiation-tolerant custom ASICs
  Nevis ADC
  LOCx2
  LOCld
FEB currently installed in USA15
Baseplane

## Slide 12: LAr Trigger Digitizer Board (LTDB)
124 LTDBs to readout the 34K Super Cells of the LAr calorimeter
1 LTDB handles analog input from 320 Super Cells
Digitizes all analog signals at 12 bits @ 40MHz using 80 custom ADC
Generate analog sums to keep compatibility with old system
Transmits digital signals using 40 optical links @ 5.12Gbps on custom ASIC
Receives TTC clock and data through 5 GBTx links
Design is made in collaboration between several groups
Phase-II compatible

## Slide 13: LTDB: NEVIS ADC
Quad 12 bits hybrid pipeline SAR ADC (IBM8RF 130nm CMOS)
40 MSPS
ENOB 11 bits
Dinamic range
  Typically 11.8 bits
Power dissipation < 50 mW/channel
112.5 ns latency
Radiation tolerant
Die:
  3.6 x 3.6 mm
  72 pins QFN

## Slide 14: NEVIS ADC: radiation tolerance
Total Dose
Single Event Effect

## Slide 15: LTDB: LOCx2 & LOCld
Layout of the LOCx2 ASIC
Layout of the LOCld
LOCx2:
Silana Foundry 250 nm, Silicon-on-Sapphire
DUAL 8 x 14 bits serializer
5.12 Gbps outputs
Nevis ADC compatible
Radiation tolerant
LOCld:
Dual channel VCSEL driver
Radiation tolerant
Die:
  2.114x1.090mm
  40 pins QFN
Power consumption 1 W
Fixed Latency < 75 ns
Die:
  6.036 x 3.68 mm
  100 pins QFN

## Slide 16: LOCx2 & LOCld: radiation tolerance
LOCx2
Eye Diagram 5.12 Gbps
2 Channels chip soldered on PCB
Total jitter ~ 50 ps (loop filter = 800 kHz)
Eye Diagram after 182 krad TID
Low or high dose rate (3krad/hr or 30 krad/h)
LOCld
No eye diagram change after 200 krad
2 channels shifted for display clarity
Current change after irradiation < 10%

## Slide 17: LTDB Development
LTDB pre-prototype 320ch
Pre-prototype PCB
  FPGA used to replace LOCx2
LTDB prototype
  Analog section and digital section are designed by different institutes, and Gerber merged for fabrication
  Power section is realized on a mezzanine
  2 LTDB prototypes could be used to replace LTDB demonstrators in January 2018

## Slide 18
Back-End (BE) Upgrade

## Slide 19: LAr Digital Processing Blade(LDPB)
Receives digital SC data from the LTDBs of the upgraded FE system, reconstructs ETSC (the transverse energy of each SC), and transmits the results to the Level-1 Calorimeter Trigger System every 25 ns.
ATCA Carrier board
4 AMC mezzanine boards
192 input fibres @ 5.12 Gbps
192 output fibres @ 11.2 Gbps
Most recent FPGAs

## Slide 20: LDPB Carrier board
RTM board
GBT SFP+
Xilinx FPGA XC7VX550T FFG1927-2
GbE
BASE Ethernet and XAUI to backplane
Main board
22 layers PCB
DC/DC
DDR
AMC connectors
IPMC
Gbe Ethernet switch
48V control brick

## Slide 21: LAr Trigger prOcessing MEzzanine: LATOME
Main DATA path
  Receives Super Cells DATA from LTDB @5.12 Gbps on up to 48 optical links
  Computes Super Cells transverse energy (ET) using optimal filter
  Builds trigger tower transverse energy
  Sends trigger tower data @11.2 Gbps on up to 48 optical links
  Sends Super Cell data to DAQ on L1A
Receives Timing Trigger & Control clock (TTC ) and data from the Carrier board
Monitors data and sends report to TDAQ system upon request on 10 GbE network
System has fixed latency less than 375 ns (15 BC)

## Slide 22: LATOME: Hardware
Altera Arria 10 FPGA (10AX115R4F40)
2Gbits DDR3 @ 800MHz
MMC controller
AMC interface
8 Avago uPods (8*12 optical links)
16 layers PCB
DC/DC block

## Slide 23: LATOME Firmware
Input stage aligns all inputs to the same BCID
Configurable remapping: reorders input data according to detector’s topology
User Code: computes Et and time using Finite Impulse Response filter (FIR)
Output summing: builds trigger tower energies

## Slide 24: Back End System Test
Connect to the real environment @CERN
TTC
ATLAS Network
Development PCs
First system test done in march 2017
Checks simple configuration
More system tests in Q2 2017
Until fully functional
Production Readines Review
Carrier boards and LATOMEs in 2017

## Slide 25
Demonstrator

## Slide 26: Demonstrator motivations
Reads data from Super Cells
Validates Energy reconstruction and bunch crossing identification
Measures trigger efficiency and jet background rejection
Gain experience in installation and operation of such equipment in the ATLAS environment

## Slide 27: FE Demonstrator: LTDB
Handles up to 320 Super Cells signals
  284 Super Cells in EM Barrel
Super Cells signals are digitized with 12bits ADC@ 40MHz
  Commercial ADC COTS : TI ADS5272 (not radiation tolerant)
Multiplexing of 8 Super Cells on one 4.8Gbps optical link
  8B10B encoding, K code sent every Bunch Crossing
  FPGA (XILINX/ALTERA)
  40 optical links
Throughput ≈200Gbps/LTDB
Status:
  2 LTDBs installed in August 2014
  Taking collision data in LHC Run 2
Digital MB + analog mezzanines
Analog MB + digital mezzanines

## Slide 28: BE Demonstrator: ABBA
ATCA board: 3 Altera FPGAs (StratixIV)
Receives up to 320 Super Cells signals (SC) from one LTDB
  48 optical links @ 4.8Gbps
Stores Super Cells data into circular buffer
  Latency up to 2.5us
Waits for TTC trigger to readout Super Cells
  Readout with filtered Level-1 trigger
Readout through 10GbE Ethernet network
  Readout with ATCA fabric interface
Status:
  3 ABBA boards installed
  Online software has been set
  Taking collision data in LHC Run 2
  Performance as expected

## Slide 29: Demonstrator installation in ATLAS
LTDB
ABBAs in ATCA crate

## Slide 30: Demonstrator data taking
Calibration:
electronic pulses sent by calibration board
Collisions (proton-proton and heavy ion):
successful data taking in 2015 and 2016:
  collected data triggered in Demonstrator region
special L1Topo trigger item used
compared Demonstrator readout and ATLAS main readout
Total noise on main readout of calorimeters cells of demonstrator (IO6) ~ neighboring crates
Plan for early 2018 to have final prototype installed and running in end of Run 2

## Slide 31
Summary

## Slide 32: Summary

## Slide 33
Backup slides

## Slide 34: Motivation and strategy
Ratio between the transverse energy of a Super Cells group of dimension 3x2 and the transverse energy of a group 7x2.
Ratio
7 GeV
~
~
2.5
ΔET
Main goals: deal with the luminosity increase, maintaining a low-pT lepton threshold and keeping the same trigger bandwidth
With the new Phase-I electronics:
Make use of shower shape variables: a more sophisticated rejection of jet backgrounds
Level-1 threshold for a given bandwidth of e.g. 20 kHz (28.5 GeV assuming Run 2 conditions) could be lowered by 7 GeV

## Slide 35: Back End System Test
  ST-M0 completed on November 2016
    Clock from FELIX well recovered on LArC and LATOME
  ST-M1 had a slight delay, ~OK on January 2017
    Good progress on firmware and software side to R&W in registers via 1GbE
  DCS monitoring completed for ST-M2 on December 2016
  ST-M3 will be the next major milestone: planned for March 2017
    Inject LTDB data, and readout FEX data for comparison
  ST-Mxx to M11: the last one to be completed ~Fall 2017

## Slide 36: Test setup
1 carrier :
  Inject « LTDB » data
  Read « FEX » data
  → data verification
  3 optical splitters 1→4 : feed the 3 other carriers
3 carriers running user code :
  compute ET for L1 (FEX)
  Send data to TDAQ via FELIX
TTC signal via FELIX
Data Monitoring via 10 GbE
Test done at EMF

## Slide 37: Number of boards
LTDB : 124
LAr Carrier : 31
LATOME : 124

## Slide 38: Planning (1)

## Slide 39: Planning(2)

## Slide 40: Phase-I Data Flow

## Slide 41: Phase-I Data Flow