## Slide 1: Phase-I Trigger Readout Electronics Upgrade for the ATLAS Liquid-Argon Calorimeters
TIPP17 –22 MAY 2017
Alessandra Camplani – Università degli Studi and INFN Milano
On behalf of the ATLAS Liquid Argon Calorimeter group

## Slide 2: Outline
Introduction
  LHC, ATLAS, LAr
  Phase I Upgrade
LAr Front End Electronics
  Baseplane, LSB
  LTDB with custom ASICs
LAr Back End Electronics
  Carrier and Latome
Demonstrator
Summary

## Slide 3
Introduction

## Slide 4: Context – LHC and ATLAS
Large Hadron Collider (LHC) at CERN, Geneva, Switzerland
  27km circumference
  depth between 50 to 175m
  four collision points
A Toroidal LHC ApparatuS: ATLAS
  46m long, 25m diameter and 7000 tons
Purpose:
  Answer fundamental physics questions about elementary particles and their interactions
Two phase upgrade planned for LHC, ATLAS upgrade:
Phase-I (2021-2023)
  upgrade of trigger path, installation in 2019-2020
Phase-II (after 2025)
  upgrade of data path, installation in 2024-2025

## Slide 5: The Liquid Argon (LAr) Calorimeter
The LAr calorimeter is a sampling calorimeter with accordion-shaped lead absorbers, Liquid Argon as active material and copper-kapton electrodes.
180k channels for the full readout of the electromagnetic (EMB+EMEC), hadronic (HEC) and Forward (FCal) calorimeters
3k channels for analog Trigger readout
Front End crates: 1524 Front End Boards (FEB)
Back End crates: 192 Readout Out Driver boards (ROD)
LAr Calorimeter played a critical role for Higgs Boson discovery with two photons as a final state.
(EMB)

## Slide 6: The current electronics
Regular (full granularity) readout:
Cells signals are amplified, shaped, sampled, digitized at 40MHz
Data are transmitted at 100 kHz upon level-1 trigger
Trigger readout:
Summing signals on Layer Sum Board (LSB)
Tower Builder Board (TBB) to form trigger towers: analog signals sent to L1 Calo system
Trigger
Tower
Regular Readout
Trigger Readout

## Slide 7: Calorimeter Upgrade
Super Cells
LAr Phase 1
Upgrade
LAr Phase-I upgrade: new calorimeter trigger electronics with increased granularity and functionality for LAr calorimeter level 1 trigger
Trigger Tower to Super Cells:
  10 times granularity increase per each trigger tower
  Information provided for each calorimeter layer for the full η range
  Finer segmentation in the front and middle layers of the EM barrel and endcap
  Higher resolution and shower information
New FE and BE electronics:
  40 MHz digitization with 12 bit precion
  Dense and high speed data transfer
  Real time data processing with a fixed latency on FPGA
Trigger Tower
Deal with the luminosity increase, maintaining a low-pT lepton threshold and keeping the same trigger bandwidth with respect to Run2

## Slide 8
Front-End (FE) Upgrade

## Slide 9: FE electronics components
New Layer Sum Boards (LSB) to perform analog sums for super cells
New Baseplane to keep compatibility with existing setup and route new SC signals
LAr Trigger Digitizer Boards (LTDB) with radiation-tolerant custom ASICs
  ADC
  Serializer (LOCx2)
  Transmitter driver (LOCld)
FEB currently installed on the detector
Baseplane

## Slide 10: LAr Trigger Digitizer Board (LTDB)
124 LTDBs to readout the 34k Super Cells of the LAr calorimeter
1 LTDB handles analog input up to 320 Super Cells
Digitizes all analog signals at 12 bits @ 40MHz using 80 custom ADCs
Generate analog sums to keep compatibility with old system
Transmits digital signals using 40 optical links @ 5.12Gbps via custom ASICs
Receive LHC clock and Trigger signals through 5 GBTx links
Analog and Digital part are merged at the gerber file level
Power section is realized on a mezzanine (PDB)
Phase-II compatible
PDB
LTDB prototype

## Slide 11: LTDB: custom ASICs (1)
ADC
Quad 12 bits hybrid pipeline SAR ADC (IBM8RF 130nm CMOS)
40 MSPS
ENOB 11 bits
Dynamic range
  Typically 11.8 bits
Power dissipation < 50 mW/channel
112.5 ns latency
Die:
  3.6 x 3.6 mm
  72 pins QFN
Status
New test board is being developed to screen and categorize the production chips quickly
180 recently produced Nevis15 chips to develop and validate the QA/QC procedures
Radiation tolerance for Nevis ADC designs was established up to ~10 MRad (requirement of 100 kRad)

## Slide 12: LTDB: custom ASICs (2)
LOCx2:
Silanna Foundry 250 nm, Silicon-on-Sapphire
DUAL 8 x 14 bits serializer
5.12 Gbps outputs
Nevis ADC compatible
Power consumption 1 W
Fixed Latency < 75 ns
Die:
  6.036 x 3.68 mm
  100 pins QFN
LOCld:
Dual channel VCSEL driver
Die:
  2.114x1.090mm
  40 pins QFN
Status:
The wafers of the baseline ASICs, LOCx2 and LOCld, have been produced and soon will be tested
Both ASICS radiation tolerant
  Irradiated up to 200 krad
  No change in the output eye diagram has been observed

## Slide 13
Back-End (BE) Upgrade

## Slide 14: LAr Digital Processing Blade(LDPB)
LDPB: receives digital SC data from the LTDBs of the upgraded FE system, reconstructs ETSC (the transverse energy of each SC), and transmits the results to the Level-1 Calorimeter Trigger System every 25 ns.
Total number of boards:
32 ATCA Carrier board and 128 AMC mezzanine (LATOME) boards
ATCA Carrier board + RTM
  Monitoring data through RTM and ATCA
4 LATOME per each Carrier
  main data flow only through LATOME
  (in: 20 Tbps, out: 41 Tbps in total)
ARRIA10 (Altera) and Virtex7 (Xilinx) FPGAs
192 input fibres @ 5.12 Gbps
192 output fibres @ 11.2 Gbps

## Slide 15: LAr Trigger prOcessing MEzzanine: LATOME
Main data path
  Receives Super Cells data from LTDB @5.12 Gbps on up to 48 optical links
  Computes Super Cells transverse energy (ET) using optimal filter at each 25 ns bunch crossing
  Builds trigger tower transverse energy and assigns it to the correct bunch crossing
  Sends trigger tower data @11.2 Gbps on up to 48 optical links
  System has fixed latency less than 375 ns
Receives Timing, Trigger Control (TTC) commands and clock and data from the Carrier board
Monitors data and sends report to Central data acquisition system upon request
DC/DC block
8 Avago uPods
(8*12 optical links)
16 layers PCB
AMC interface
2Gbits DDR3 @ 800MHz

## Slide 16: Back End System Test
Build a system with the final prototype
Connect to the real environment @CERN
Timing, Trigger Control commands and clock
Atlas Development Network
Development PCs
First system test done in march 2017
Checks simple configuration
More system tests in Q2 2017
Until fully functional
Purpose
Confirm all functionalities before mass production

## Slide 17
Demonstrator

## Slide 18: Demonstrator motivations
Reads data from Super Cells
Validates energy reconstruction and bunch crossing identification and collects real collision data for the filtering algorithm development
Gain experience in installation and operation of such equipment in the ATLAS environment
A demonstrator was installed in ATLAS in the EM barrel (coverage 1/32 of barrel region) in summer 2014 to show the feasibility of the Phase I Upgrade:
Demonstrator FE: 2 LTDBs
Demonstrator BE: 3 (originally 2) ATCA test Board for Baseline Acquisition (ABBA)

## Slide 19: FE Demonstrator: LTDB
Handles up to 320 Super Cells signals
  284 Super Cells in EM Barrel
Super Cells signals are digitized with 12bits ADC@ 40MHz
  Commercial ADC COTS : TI ADS5272 (not radiation tolerant)
Multiplexing 8 Super Cells on one 4.8 Gbps optical link
  8B10B encoding, K-code sent every Bunch Crossing revolution
  Xilinx FPGAs
  48 optical links
Throughput ≈ 200 Gbps/LTDB
Status:
  2 LTDB versions developed and installed in August 2014
  Taking collision data in LHC Run 2
Digital Motherboard + analog mezzanines
Analog Motherboard + digital mezzanines

## Slide 20: BE Demonstrator: ABBA
ATCA board: 3 Altera FPGAs (Stratix IV)
Receives up to 320 Super Cells signals (SC) from one LTDB
  Up to 48 optical links @ 4.8Gbps
Stores Super Cells data into circular buffer
  Latency up to 2.5us
Waits for Level-1 trigger to readout Super Cells data
Readout using IPbus protocol over UDP on 10 GbE network
  Readout with ATCA fabric interface
Status:
  3 ABBA boards installed in USA15
  Online software operational
  Concurrent readout in parallel with ATLAS default readout since October 2015
  Since November 2016 integrated in the automated ATLAS data taking
  Successful data taking in LHC Run 2
Altera FPGAs
DC/DC
Optical links
IPMC
16 layers PCB

## Slide 21: Demonstrator data taking
Calibration:
electronic pulses sent by calibration board
Collisions (proton-proton and heavy ion):
successful data taking in 2015 and 2016:
  collected data triggered in Demonstrator region
in-system debugging of firmware quite successfully
  ready for 2017 pp data taking
special Level-1 topological trigger item is used
  thanks to the L1 community
compared Demonstrator readout and ATLAS main readout
Noise levels of SCs
Calibration pulse shape
Total noise on main readout of calorimeters cells of demonstrator similar to neighboring crates
Plan for early 2018 to have final prototype installed and running in end of Run 2

## Slide 22
Summary

## Slide 23: Summary
The ATLAS Lar calorimeter electronics will be upgraded for Phase-1 after Long Shutdown 2 (2019-2020)
The trigger path will be digitized at Front-End level with an improved granularity
LTDB and LDPS systems are being developed and produced
  Radiation tolerant ADC and Optical links specifically designed
  System input data rate is 20Tbps and output data rate is 41 Tbps in total
  LTDB prototype being assembled
  LDPB ATCA carrier board and LATOME AMC boards being tested
A part of the new Trigger scheme (Demonstrator) has been installed
  Both Front End and Back end electronics have been validated
  One Front End Crate (1/32) is equipped with the demonstrator
  Readout through TDAQ software
Production will start in 2018

## Slide 24
Backup slides

## Slide 25: LHC Schedule
Two phase upgrade planned for LHC, ATLAS upgrade:
Phase-I (2021-2023): upgrade of trigger path, installation in 2019-2020
  (Average number of vertices per bunch crossing)
  Keep trigger max 100 KHz, latency
Phase-II (after 2025): upgrade of data path, installation in 2024-2025
  (Average number of vertices per bunch crossing)
  Keep trigger max 1 MHz, latency
Upgrade of LAr trigger readout
Upgrade of LAr main readout

## Slide 26: ADC: radiation tolerance
Single Event Effect
Total Ionizing Dose

## Slide 27: LOCx2 & LOCld: radiation tolerance
LOCx2
Eye Diagram 5.12 Gbps
2 Channels chip soldered on PCB
Total jitter ~ 50 ps (loop filter = 800 kHz)
Eye Diagram after 182 krad TID
Low or high dose rate (3krad/hr or 30 krad/h)
LOCld
No eye diagram change after 200 krad
2 channels shifted for display clarity
Current change after irradiation < 10%

## Slide 28: LTDB Development
LTDB pre-prototype 320ch
Pre-prototype PCB
  FPGA used to replace LOCx2
LTDB prototype
  Analog section and digital section are designed by different institutes, and Gerber merged for fabrication
  Power section is realized on a mezzanine
  2 LTDB prototypes could be used to replace LTDB demonstrators in January 2018

## Slide 29: LATOME Firmware
Input stage aligns all inputs to the same BCID
Configurable remapping: reorders input data according to detector’s topology
User Code: computes Et and time using Finite Impulse Response filter (FIR)
Output summing: builds trigger tower energies

## Slide 30: Demonstrator readout in ATLAS
LTDBs in FE crate
ABBAs in ATCA crate
with 10GbE ethernet switch
ATLAS LAr TDAQ software
Readout computer (10GbE)
#1
#2
#3
UX15
USA15