## Slide 1: Phase-I Trigger Readout Electronics Upgrade for the ATLAS Liquid-Argon Calorimeters
TIPP17 – ? MAY 2017
Alessandra Camplani – Universita’ degli studi and INFN Milano
On behalf of the ATLAS Liquid Argon Calorimeter group

## Slide 2: Outline
Introduction and conte
  LHC, ATLAS, LAr
LAr Phase-I Upgrade Project
  LAr Demonstrator
  Baseplane and LSB
  Front End: LTDB
    ASICs
    Development
  Back End: LDPS
    AMC
    Carrier
Summary

## Slide 3
Introduction

## Slide 4: Context – LHC and ATLAS
Large Hadron Collider (LHC) at CERN, Geneva, Switzerland
  27km circumference
  depth between 50 to 175m
  four collision points
ATLAS: A Toroidal LHC ApparatuS
  46m long, 25m diameter and 7000 tons
Purpose:
  Answer fundamental physics questions
  Standard model

## Slide 5: The Liquid Argon (LAr) Calorimeter
The LAr calorimeter is a sampling calorimeter with accordion-shaped lead absorbers and copper-kapton electrodes.
180K channels for the full readout of the electromagnetic (EMB+EMEC), hadronic (HEC) and Forward (Fcal) calorimeters
3K channels for analog Trigger readout
Front End crates: ≈ 1600 Front End Boards (FEB)
Back End crates: 200 Readout Out Driver boards (ROD)

## Slide 6: Why we need an upgrade
Increasing luminosity and increasing number of events
With the augmented luminosity the events (electrons and photons) selected by the calorimeter trigger would be about 270 kHz with the present system
This number must be reduced to 20 kHz
Isolation techniques at trigger level are not sufficient any more: some upgrades on the trigger are needed

## Slide 7: Calorimeter structure
Four layers: presampler, front, middle and back.
Each layer is made of elementary cells which correspond to the real calorimeter granularity
From the trigger point of view:
Towers: existing trigger granularity
Super Cells: Phase I trigger granularity

## Slide 8: Calorimeter Upgrade
Trigger Tower
Super Cells
LAr Phase 1
Upgrade
LAr Phase-I upgrade: new calorimeter trigger electronics with increased granularity and functionality for LAr calorimeter level 1 trigger
Trigger Tower to Super Cells:
  Granularity increased 10 times per each trigger tower
  Provided information for each calorimeter layer for the full η range
  Finer segmentation in the front and middle layers of the EM barrel and endcap
  Higher resolution and shower information
Deal with the luminosity increase, maintaining a low-pT lepton threshold and keeping the same trigger bandwidth

## Slide 9: Current system
Electronics to be addressed
for Phase-I Upgrade
Schematic block diagram of the current LAr readout electronics architecture.
The LAr ionization signal proceeds upwards, through the FE crates mounted on the detector to the BE electronics in the USA15.

## Slide 10: LAr Phase-I Project
Baseplane
Layer Sum Board
(LSB)
LAr Trigger Digitizer
Board (LTDB)
LAr Digital Processing System (LDPS)
New elements are highlighted in RED

## Slide 11
LAr Phase-I Upgrade Project

## Slide 12: Demonstrator
Demonstrator installed in summer 2014
  2 LTDBs readout via ABBA boards
Successful 2016 ATLAS pp data taking
No L1Topo during HI period
  LArABBA partition active for some runs, triggering on Physics + Calo
Development and analysis works are making progress
  Continuous development on firmware and software
    Corrected latency shift happening during long runs
    Introduce ID for tracing packets between FPGAs
    Integration of ABBA as a new segment of ATLAS

## Slide 13: Baseplane
FDR of Baseplanes : 30 June 2015
EMB and EMECStd full contract awarded, first item to arrive around the end March 2017 (100 pcs)
  PRR to release production around April 2017
HEC prototype done, advance testing, preparing production (8 pcs)
FCAL side A prototype under test. FCAL side C needs a modified design (2 pcs)
EMEC SP Prototype in fabrication (8 pcs)
Manufacturer identified for RF springs (original 2005 vendor dismissed), trying to pass full PO from CERN

## Slide 14: Layer Sum Board
FDR of LSBs: 30 June 2015
First part of LSB PRR on July 19 2016:
  https://indico.cern.ch/event/547081/
Second part of LSB PRR on October 19 2016:
  https://indico.cern.ch/event/574104/
All qualifications done
Single lot opamps ordered and arrived
LSBs production ongoing
FEB currently
installed
in USA15

## Slide 15: LTDB: ADC
Nevis13 - Nevis14: found digital issue (2015), ADC producing “bad codes” = “spikes” @~10 Hz
Nevis15 chip: “minimal” modification (no analog changes)
Available March 2016 and tested on 64 channels board: OK
  QA to select good chips
Mini-production end 2016 for ~180 chips for the assembly of LTDB prototypes
Calibration test with sine waveform
PDR of ADC (May 2014) : use Nevis ASIC
  Power, latency gain

## Slide 16: LTDB: LOCx2 & LOCld
LOCx2 (Serializer) / LOCld (opt. Link)
  Baseline option 250 nm SOS (Silicon On Sapphire)
  4 different processed wafers received on August 2016 : OK, minor yield differences
  Ordered full production of 20 wafers: 16/20 OK.
    Dies starting to be packaged now.
    Should have proof of functioning at the end of February
If all OK (yield ~> 50%), sufficient chips in hand next months
QA plans in preparation and radiation tests to be repeated
We had some issues on production in the past: - Started a backup solution with 130 nm CMOS technology - LArTDS: serializer based on GBTx Ip - Chips delivered, currently under test and first operation seems OK
Layout of the LOCx2 ASIC
Layout of the LOCld

## Slide 17: LTDB Development
LTDB 64ch prototype
  Fully tested
  Checked all chip control
    GBTx, GBT-SCA, MTx, MTRx
    Nevis14 - Nevis15
  Also September LOCx2, all OK
  Confidence building for 320 channels prototype
LTDB pre-prototype 320ch
  Design Integration learning
  Large board manufacturing
  Analog performance check @ Saclay
  Digital Readout tested at BNL with FELIX board

## Slide 18: LTDB Development (2)
LTDB prototype
  Gerber merged at the end of December
  Some delay came from details Milano/Saclay/BNL for the PDB (Power Distribution Board) pins + monitoring signal
  PCBs received Jan 31st. Board expected end February
  Tests in ~March @ BNL, @ Saclay
  AIM: 2 LTDB prototypes could be used to replace LTDB demonstrators in January 2018
Power Distribution Board (PDB)
  Previous design based on FEAST device from CERN, current design based on LTM4619 (COTS), development on going (Milano)
  PDB design and submission by end February 2017
Joint test LTDB-PDB (expected April 2017) will define FE reviews
  FDR of LTDB, PRRs of ASICS (~May 2017)

## Slide 19: LDPS Development
Carrier board V1 2015, FDR passed with AMC
  V2 available since Spring 2016
    On board Ethernet HW chip
  V3 already assembled
    Test ongoing
    To be used in further integration
Fibers: work in progress for pre-series
LATOME V2
LATOME
  Based on Altera Arria10 FPGA
  LATOME V1 is working, but with some power issues
    Design has been updated
  LATOME V2 ready at the end of 2016: is working fine and power issue seem fixed
    FPGA core current decreased
    Setup power decreased -> More firmware for the same power
Setup power / Nb of FIR samples
FPGA temperature / Setup power
LATOME V2
LATOME V2

## Slide 20: LDPS Firmware
LATOME firmware development ongoing
  Block deliverables:
    Seven groups contributing
  Emphasis on simulation and integration
  Latency and resources verified at each major step
  Adapt to System Test milestones : implement on HW
Carrier firmware development ongoing
  Development of Carrier firmware continues with emphasis on completing a baseline project
  Testing of Carrier hardware and firmware at EMF will be ongoing (TTC, 1GbE, 10GbE etc.)
  Stability issue of uBlaze project to be addressed

## Slide 21: Back End System Test
Demonstrate feasibility of BE system
  Pass PRR for releasing series board production
  Show operation of all parts of system
  Verify operation of FPGAs
  Test Power-Cooling in ~final conditions
  Boost coding, testing and debugging of FW
  Boost coding, testing and debugging of Online SW (incl. TDAQ)
  Eventually connect to LTDB
    Full system test
Several milestones have been reached: moving forward for the next steps
PRR expected in late spring

## Slide 22
Summary

## Slide 23: Summary
LAr Demonstrator has successful 2016 ATLAS pp data taking
  Preparation for 2017 run has started
Baseplane is making progress
  Manufacturer identified for RF springs, trying to pass full PO from CERN
LSBs production ongoing
  Passed PRR in October successfully
Front end LTDB
  Nevis15 ADC tested on 64 channels board and OK, plan to address it by QA
  LOCx2 16/20 wafer are ok, proof of functioning at the end of February
  LTDB board development is progressing well with baseline design: FDR by spring 2017
Back end LDPS
  LATOME V2 much improved in terms of power, temperature and voltage drop vs V1
    cabling of 13 boards in process and fibers being ordered
    12 LATOME V2 boards should be available for the system test by end of March
  Carrier V3 assembled and test ongoing
  Firmware development is making good progress and BE system integration is marching to the next major milestone

## Slide 24
Backup slides

## Slide 25: Motivation and strategy
Ratio between the transverse energy of a Super Cells group of dimension 3x2 and the transverse energy of a group 7x2.
Ratio
7 GeV
~
~
2.5
ΔET
Main goals: deal with the luminosity increase, maintaining a low-pT lepton threshold and keeping the same trigger bandwidth
With the new Phase-I electronics:
Make use of shower shape variables: a more sophisticated rejection of jet backgrounds
Level-1 threshold for a given bandwidth of e.g. 20 kHz (28.5 GeV assuming Run 2 conditions) could be lowered by 7 GeV

## Slide 26: LAr Demonstrator
Development and analysis works are making progress
Continuous development on firmware and software
  Corrected latency shift happening during long runs
  Introduce ID for tracing packets between FPGAs
  Integration of ABBA as a new segment of ATLAS
Calibration data taking has been carried out
New Ntuples format for demonstrator data

## Slide 27: Back End System Test
  ST-M0 completed on November 2016
    Clock from FELIX well recovered on LArC and LATOME
  ST-M1 had a slight delay, ~OK on January 2017
    Good progress on firmware and software side to R&W in registers via 1GbE
  DCS monitoring completed for ST-M2 on December 2016
  ST-M3 will be the next major milestone: planned for March 2017
    Inject LTDB data, and readout FEX data for comparison
  ST-Mxx to M11: the last one to be completed ~Fall 2017

## Slide 28: Test setup
1 carrier :
  Inject « LTDB » data
  Read « FEX » data
  → data verification
  3 optical splitters 1→4 : feed the 3 other carriers
3 carriers running user code :
  compute ET for L1 (FEX)
  Send data to TDAQ via FELIX
TTC signal via FELIX
Data Monitoring via 10 GbE
Test done at EMF

## Slide 29: Number of boards
LTDB : 124
LAr Carrier : 31
LATOME : 124

## Slide 30: Planning (1)

## Slide 31: Planning(2)

## Slide 32: Phase-I Data Flow

## Slide 33: Phase-I Data Flow

## Slide 34
Nicolas Dumont Dayot

## Slide 35
Nicolas Dumont Dayot
Nicolas Dumont Dayot

## Slide 36
Nicolas Dumont Dayot

## Slide 37
Nicolas Dumont Dayot

## Slide 38
Nicolas Dumont Dayot

## Slide 39
Nicolas Dumont Dayot

## Slide 40
Nicolas Dumont Dayot