## Slide 1: TTC status
Alessandra Camplani – Università degli Studi e INFN Milano
12/01/2017

## Slide 2: Available/requested/missing signals
In contact with Ken to provide the proper signals (on the proper interface) to the TDAQ/Mon block.
The discussion is on going on this Jira ticket: LDPBFW-25
Signals already in the TTC code:
L1A
EVID and BCID
TType
What is currently being prepared:
TType cnt (simulation almost ok, needs still some checks)
Interface-related signals (not yet done)

## Slide 3: Reminder: EVID and BCID
BCID: 12 bit vector
Counting on a 40MHz clk
Every time that a BCR signal is received the counter is reset to zero (max value is 3564)
  (The BCR is sent at the end of each LHC cycle in order to reset the bunch crossing counter)
EVID: 32 bit vector made of two counters
31 downto 24: ECR sub-counter
23 downto 0: L1A sub-counter
How to count:
Every time that an ECR is received the ECR sub-counter is increased while the L1A sub-counter is set to 1
Every time that a L1A is received the L1A sub-counter is increased

## Slide 4: TType counter
TType counter, as requested by Ken, should match the L1A counter (per each L1A there is a TType on the Bchannel).
The TType counter will match with the lower part of the EVID (24 bit L1A sub-counter).
As said before, every time that an ECR is received the L1A sub-counter is set to 1:
the TType counter can’t be reset when the ECR is received
  L1A and TType are not received simultaneously: the L1A is received and after a not-fixed delay the TType info is received, so they can’t be reset at the same time by the incoming ECR
  The last value of the L1A sub-counter (before the ECR reset) is recorded: this is compared with the counter value for the TType
  Once the two values (L1A counter and TType counter) are equal the TType counter is reset
  A new signal is generated to clean the recorded L1A sub-counter value to FFFFFF

## Slide 5: TType counter: simulation
Code and simulation files are all on git

## Slide 6: Conclusion
Firmware point of view
Discussion about the missing signals for the TDAQ/mon block is on going : LDPBFW-25
  TType counter is almost done
Send signals on 240 MHz clk
  Created a ticket for the new clk: LDPBFW-787
AV_ST interface to be prepared
Hardware test not yet done
Bernard is able to see L1A, ECR, BCR (what’s the difference between Bernard’s and Carrier code?)
Bchannel has still some issues but Andrea Borga (FELIX) is working on it
Discussion on going on Jira ticket: FLXUSERS-47