## Slide 1
Firmware updates
Alessandra Camplani – Università degli Studi di Milano

## Slide 2
Extra padding data
Problem of extra padding data: SOLVED
Request
From the PC
Front FPGA
UDP module
Back FPGA firmware
Extra padding data
NO extra padding data
Correct response for commands:
FPGA_Id
firmware_version

## Slide 3
Still some errors
Command: write_counter
After this command, FPGA_Id and firwmare_version commands don’t work anymore.

## Slide 4
State machine with SignalTap
State machine (front FPGA firmware, response to the IPbus): comparison between the correct and the un-correct behaviour:
Board in slot 2 (168.192.10.3)
  FPGA_Id command
Board in slot 4 (168.192.10.4)
  Write_counter command
  FPGA_Id command
So, the same IPbus packet is sent to the front FPGA.
It is possible to notice a complete different behaviour.

## Slide 5
State machine with SignalTap
State machine (front FPGA firmware, response to the IPbus): comparison between the correct and the un-correct behaviour:
Board in slot 2 (168.192.10.3)
  FPGA_Id command
Board in slot 4 (168.192.10.4)
  Write_counter command
  FPGA_Id command
So, the same IPbus packet is sent to the front FPGA.
It is possible to notice a complete different behaviour.

## Slide 6
Strange commands behaviour
SOMETIMES
Sending the same command after re-loading the firware on both FPGAs

## Slide 7
Conclusions
State machine problem solved: there was a missing register signal in the firmware
The strange behaviour is probably due to the fact that the FPGA is not yet in a «locked state»
The front FPGA state machine must be modified to avoid a bad response from FPGA