## Slide 1
Firmware updates
Alessandra Camplani – Università degli Studi di Milano

## Slide 2
Test at EMF
New firmware tested at EMF:
v0.95a for the front FPGAs
v0.68 for the back FPGAs
The standard configuration for the connection between the ABBA front FPGAs and the LTDB is shown in figure:
FPGA0 from board 10.3
FPGA1 from board 10.4
But FPGA0 on ABBA 10.3 has a bit flip in JTAG chain, so there is a failure during the programming procedure.
FPGA1
FPGA0
Back
168.192.10.3
FPGA1
FPGA0
Back
168.192.10.4
BNL LTDB

## Slide 3
Test at EMF
New firmware tested at EMF:
v0.95a for the front FPGAs
v0.68 for the back FPGAs
The standard configuration for the connection between the ABBA front FPGAs and the LTDB is shown in figure:
FPGA0 from board 10.3
FPGA1 from board 10.4
But FPGA0 on ABBA 10.3 has a bit flip in JTAG chain, so there is a failure during the programming procedure.
The configuration with the LTDB has been changed:
FPGA1 from board 10.3
FPGA1 from board 10.4
FPGA1
FPGA0
Back
168.192.10.3
FPGA1
FPGA0
Back
168.192.10.4
BNL LTDB
Laura did some tests at EMF and the firmware is stable: no need to reprogram the FPGAs

## Slide 4
Test in USA15
Also in USA15, new firmware tested:
v0.95a for the front FPGAs
v0.68 for the back FPGAs
Adriana did some tests but the firmware (the same used in EMF) is still not stable
FPGA0 from ABBA 91.18 is sending some random data that affect FPGA1 on the same board, but also the other board:
FPGA0 on ABBA 91.18 continuously sends random data (data and addresses not known)
Back FPGA tries to identify the addresses and sends a broadcast request to all the other modules (also to the other ABBA board)
No one is recognising the addresses: the system is blocked
FPGA1
FPGA0
Back
10.45.91.18
FPGA1
FPGA0
Back
10.45.91.19
?

## Slide 5
Conclusions
Behaviour of FPGA0 from board 91.18: investigating..
Broadcast problem: can be solved with some changes in back FPGA firmware
Simulation for the IPbus reception in front FPGA ready
Next step: modify front FPGA state machine to avoid bad responses from FPGA