## Slide 1: TTC status
Alessandra Camplani – Università degli Studi di Milano
12/5/2016

## Slide 2: Data on LVDS links: proposal
LVDS link #1
The signal is high when the transmission is valid.
LVDS link #2
HL: stands for high/low
  In the first packet HL = 1, in the second packet HL = 0, in the third packet HL = 1.. and so on.
  It's a sort of alignment bit, reserved to start and synchronize words.
  If nothing is sent, HL continues to switch from 1 to 0.
L: is the L1A bit.
E: is the ECR bit.
B: is the BCR bit
4 LVDS links available:

## Slide 3: Data on LVDS links: proposal
LVDS link #3 and #4
HL: is, again, the alignment bit
  It has the same value of the HL used in link 1 and 2 (to ensure the alignment between channels)
  If nothing is sent, HL continues to switch from 1 to 0.
D#: allow to build longer words for "other" data
  D0, D1 .. D7 can be an 8 bit word.
  When no data are sent all D are set to 0.
XY: is a counter.
  The counter is XY=11 when the first packet is sent, it is XY=10 for the second packet, XY=01 for the third packet and XY=00 for the fourth. This counter will allow to build words up to 16 bit. If nothing is sent the counter is in 00 state.

## Slide 4: Conclusion
Proposal for the LVDS link format
  (thanks to Steffen and Nicolas(s) for the suggestions)
Started implementing a “decoder” for this LVDS format
Simulation is also ongoing