## Slide 1
ABBA firmware status
Alessandra Camplani – Università degli Studi di Milano
06/06/2016

## Slide 2
Firmware version
2
Last firmware versions presented during the Upgrade Week in April 2016:
front FPGA: v0.95b
back FPGA: v0.68a
For more details
Upgrade Week: ABBA firmware status
Current versions used to take data:
front FPGA: v0.96
back FPGA: v0.69a

## Slide 3
Improvements in front FPGA
3
Test firmware version: v0.95b1
  Solved "critical warnings" for timing constraints and improved reset structure in front fpga firmware
Test firmware version: v0.95b2
  Changed reset from asynchronous to synchronous in front FPGA top level processes
Test firmware version: v0.95b3
  Reorganisation of writing procedure for front FPGA registers (to simplify the code)
Test firmware version: v0.95b4
  Combination of writing and reading procedure for registers: new entity defined (to simplify the code)
Test firmware version: v0.95b5
  Changed reset from asynchronous to synchronous in IPBUS front FPGA files
After some tests, v0.95b5 (test) upgraded to production version v0.96

## Slide 4
Known issue with FPGA 18:0 in USA15 (part 1)
4
Front
FPGA
1
Front
FPGA
0
Back
FPGA
18
In USA15:
two “identical” ABBAs
3 “identical” FPGAs per board (all Stratix IV from ALTERA)
  2 front FPGAs
  1 back FPGA
All 4 front FPGAs using the SAME firmware version:
only one not responding (FPGA 18:0)
Reminder from ATLAS Upgrade Week:
FPGA 0 from ABBA 91.18 was sending some random data that affect FPGA 1 on the same board, but also the other board
  v0.68a: length check in UDP and IP module now avoids transmission of garbage!
    Stabilized readout with 3 remaining FPGAs
Front
FPGA
1
Front
FPGA
0
Back
FPGA
19

## Slide 5
Known issue with FPGA 18:0 in USA15 (part 2)
5
Front
FPGA
1
Front
FPGA
0
Back
FPGA
18
Issue hidden but not solved …
Looking with Signal Tap Altera tool in front FPGA:
the signal which is blocking if the FPGA is aligned_status:
  coming from the ALTERA XAUI CORE
  connected to channelaligned signal in the back FPGA interface
The issue is coming from the communication between front and back FPGA.
Front
FPGA
1
Front
FPGA
0
Back
FPGA
19

## Slide 6
Known issue with FPGA 18:0 in USA15 (part 3)
6
All these attempts didn’t solve the issue.
Last chance was:
Two pairs of XAUI transceivers interconnecting front and back FPGAs on ABBA
Tried the second XAUI transceiver
Neither this solution recovered the FPGA.
Conclusion: hardware issue (also the TTC is behaving differently here!)
Finally (27/05/2016): added a new ABBA in USA15 to substitute FPGA 18:0
Front
FPGA
18:1
Front
FPGA
18:0
Back
FPGA
Default XAUI links
New XAUI link used
Second XAUI link
To solved this issue different strategies have been adopted:
Solved timing critical warnings
Used a different (better) clock source: oscillator
Improved reset structure
Changing reset in most important processes from asynchronous to synchronous

## Slide 7
Improvements in back FPGA
7
Firmware version v0.69:
  Back FPGA STP file and constraint files reworked:
    - no more timing warnings
    - no more unconstrained paths
    - no complaints of unconnected signals in Signal Tap
  Minor update in interface merger process (sensitivity list) for ready signal
Firmware version v0.69a:
As said before, another board has been installed in USA15.
New IP and MAC addresses added in the firmware.
Added a new item to the MAC_IP_selector generic:
selects the pair of MAC and IP address of the Back FPGA
IP -.19
IP -.18
IP -.20
Actually back FPGAs with IP -.18 and -.19 are using (and can remain with) version v0.69.
Only FPGA with IP -.20 is using version v0.69a.

## Slide 8
Conclusion and outlook
v0.69a for the back FPGA and v0.96 for the front FPGA: STABLE!
  No needs to reprogram the FPGAs during the data taking
Issue with FPGA 0 on ABBA 91.18 in USA15
  After many trials new (Oregon) board installed
    Previously installed in EMF
  No firmware (or hardware) issues on the new board
Collecting data with all 4 FPGAs
Next step:
  Some data already analysed: found bad readings
    To be investigated …
8